## Slide 1
HST Rough Toolpaths

## Slide 2: Cut Parameters
Note: The cut parameters will change based on the toolpath type. When possible the same settings will be brought into the new toolpath type.

## Slide 3: Cut Parameters
Add cuts- Activates the adaptive stepdown feature, which add cuts at the shallow areas of the profile so that the toolpath does not have excessively large horizontal spacing between cutting passes
Min stepdown – Specifies the minimum stepdown value when Add cuts is activated. Passes will be no less than this distance from each other – in the z axis
Stepdown – Determines the Z spacing between adjacent cutting passes
Turn on the “Add cuts” option

## Slide 4: Cut Parameters
Max profile stepover – is the thickness of the scallop. If the thickness exceeds the .250 setting then a z cut is added to bring the thickness under the .250 setting.
Max profile stepover – Determines the maximum change in the surface profiles for two adjacent cutting passes. This represents the maximum value of the shortest horizontal distance between adjacent points on the two profiles.

## Slide 5: Cut Parameters
Notice the scallop thickness

## Slide 6: Cut Parameters
Max profile stepover

## Slide 7: Cut Parameters
Smoothing – Replaces sharp corners with an arc for faster and smoother transitions in the tool direction.
Turn on the “Smoothing” option

## Slide 8: Cut Parameters
Profile Tolerance – The maximum distance that the outermost profile of the smoothed toolpath that will deviate from the original toolpath
Offset tolerance – This is the same measurement as the profile tolerance but is applied to all of the profiles except the outermost one. This lets you maintain different tolerances for the subsequent profiles.
Max Radius – Enter the radius of the largest arc that you will allow Mastercam to insert to replace the corner. Larger arcs will result in a smoother toolpath but with greater deviation from the originally programmed toolpath

## Slide 9: Cut Parameters
Possible to leave different amounts of stock for floor and wall surfaces.
Note: Can’t leave less stock on the walls than the floor

## Slide 10: Cut Parameters

## Slide 11: Transition
Use this page to configure the entry move that the tool will make as it transitions to new Z levels.
Note: Core Roughing, Area Clearance, Rest Roughing and Horizontal use these parameters

## Slide 12: Transition
Note: If tool can’t fit with Helical Entry settings then Ramp Entry is used.
Radius - Enter the radius of the entry helix. If the profile is too small for a helix ramp of this diameter, Mastercam will create a profile ramp instead.
Output arc moves - Select this option to have Mastercam create the helix with arc moves. De-select this option the helix will be rendered with many small linear moves.
Z Clearance - This is an extra height used in the ramping motion down from a top profile.
Plunge angle - The ramps into the cut will be no greater than this value

## Slide 13: Transition
Z clearance - This is an extra height used in the ramping motion down from a top profile
Plunge angle - The ramps into the cut will be no greater than this value.
Preferred profile length - Enter a minimum size for the profile in order for a ramp to be created.
Skip pockets smaller than - Use this value to specify a minimum distance across the pocket that Mastercam will consider creating a cutting pass for.

## Slide 14: Transition
Preferred profile length
Top View
Iso View

## Slide 15: Transition
Preferred profile length
Top View
Iso View

## Slide 16: Transition
Note: Both “Entry Helix” and “Profile Ramp” both use these settings

## Slide 17: Steep/Shallow
Z Depth

## Slide 18: Steep/Shallow
Use Z depths - Select this option to limit the machining zone to the area between the depths entered in this section.
Detect limits- Automatically populate the Minimum and Maximum depth fields with the highest and lowest points on your drive surfaces.

## Slide 19: Linking Parameters
Linking - Use this page to create the links between the cutting passes. In general, you can think of linking moves as air moves when the tool is not in contact with the part.

## Slide 20: Linking Parameters
Retracts - This determines how the tool will move between the end of one pass and the beginning of another
The “Curl up” and ‘Curl Down” will be grayed out unless “Minimum Distance” is selected.

## Slide 21: Linking Parameters
6
1
2 & 5
3
4

## Slide 22: Linking Parameters
Min Distance - Inserts Curl up / Curl down high-speed arcs (.1683) to and from the retract height and maintains a Part clearance (.153) above the surface for the fastest transitions

## Slide 23: Linking Parameters

## Slide 24: Linking Parameters
Min Distance

## Slide 25: Linking Parameters
Output feed move - Use this option to output the rapid move between passes as a feed rate move.
Note: Since each machine is going to have a different max feed rate, this value is set from the machine definition.

## Slide 26: Linking Parameters
Output Feed move setting

## Slide 27: Linking Parameters
Part Clearance
Minimum Vertical Retract – The tool retracts only as high as it needs to, to clear the part by the “part clearance” setting

## Slide 28: Linking Parameters
Full Vertical Retract – The tool retracts to the “Clearance plane”
Full Vertical Retract

## Slide 29: Linking Parameters

## Slide 30: Linking Parameters
Machine Entire Pass (finishing) –The path of the tool will match the surface, including vertical surfaces and the corners. An entry/exit arc will only be inserted at the end of the pass, and then only if it can be done safely without hitting the part.
Minimize Trimming (roughing) – The path of the retract will be as close to the surface as possible, maintaining a minimum distance from the surface to fit the entry/exit arc.
Fully Trim Pass (?)– Fully trim pass—The pass is trimmed back so the entire entry/exit arc fits into it, but no nearer than a full machine pass link would be. Select this option where it is important to prevent over-machining.

## Slide 31: Reference Points

## Slide 32: Reference Points
Reference point - is a location that the tool moves to between the home (tool change) position and the start or end of the toolpath. You can create separate reference points for both approach and retract moves.

## Slide 33
Arc Filter/Tolerance

## Slide 34
Filter ratio - The ratio of filter tolerance to cut tolerance. This ratio is automatically applied to the filter tolerance and cut tolerance. If Off, then Mastercam uses only the cut tolerance for the toolpath.
Arc Filter/Tolerance

## Slide 35
Arc Filter/Tolerance
Toolpath Fillets: Theoretical fillets are created in sharp corners to keep the tool motion smooth and allow flat cutters to be used in roughing where fillets weren’t created in the model.

## Slide 36
No toolpath fillets
Arc Filter/Tolerance

## Slide 37
Toolpath Fillets
Arc Filter/Tolerance

## Slide 38
Planes (WCS)

## Slide 39
Coolant

## Slide 40
Canned Text

## Slide 41
Miscellaneous Values

## Slide 42
Axis Combination

## Slide 43
Toolpath Type
Use a rest roughing toolpath when you want to calculate the cutting passes only on the stock left over from one or more previous roughing operations, similar to Restmill
Rest Roughing

## Slide 44
Rest Roughing
Rest Material

## Slide 45
Rest Material
All previous operations - Calculates the remaining stock using all operations in the Toolpath Manager. This method determines the areas of stock where the tool did not go.
One other operation - Calculates the remaining stock using all operations in the Toolpath Manager. This method determines the areas of stock where the tool did not go.
Roughing tool - Calculates the remaining stock based on the diameter and corner radius of a tool.
Cad file – Uses an STL file to calculate where the tool can remove material

## Slide 46
Lists the current operations in the operation manager
Rest Material

## Slide 47
Stock resolution - Use a smaller value to tighten up the stock model and create a smoother restmill toolpath. Use a larger value to loosen the stock model and create a faster but rougher restmill toolpath.
Rest Material

## Slide 48
Adjustments to remaining stock
Use remaining stock as computed – No adjustment to the stock model
Adjust remaining stock to ignore small cusps – Use this setting to set the adjustment distance to reduce the stock model, this setting will find less material to machine
Adjust remaining stock to mill small cusps – Use this setting to set the adjustment distance to increase the stock model, this setting will find more material to machine
Rest Material

## Slide 49
Adjustments to remaining stock
Adjustment distance - Enter a value to expand or reduce the calculated stock model
Rest Material

## Slide 50
Roughing tool is a theoretical calculation.
Note: With the “Skip pocket” setting its possible to have the tool plunge into material with the “Roughing Tool” setting
Rest Material

## Slide 51
An STL file can be used to calculate remaining stock. Verifying a toolpath and then saving the stock as an STL may give a more accurate results.
Rest Material