## Slide 1: CheckHolder
Open file: Check Holder.mcx

## Slide 2: CheckHolder
What does Checkholder do?
Calculate the require tool length for an operation.
Find any interferences that the toolholder will have with the part
Generate additional tools and operations for deeper area’s that the original tool couldn’t reach.
  Example: If the tool length is 1 inch, and the required length is 1 ½ inches then a 1 ¼ and a 1 ½ tools are created along with an separate operation for each tool.

## Slide 3: CheckHolder
#1 – To find the required tool length for the toolpath
?

## Slide 4: CheckHolder
Select the operation that you want to check. Only one operation can be checked at a time.

## Slide 5: CheckHolder
Hit “Alt-C” to bring up the C-hook list and select CheckHolder.dll

## Slide 6: CheckHolder
Go into “Preferences”

## Slide 7: CheckHolder
Select “Single tool”
The “Single tool” setting is for calculating the required tool length of the tool to reach the programmed toolpath.

## Slide 8: CheckHolder
The “Multiple tools” is used for creating additional operations with addition tools. Each tool will be “.250 “ longer than the previous tool until the entire toolpath can be reached

## Slide 9: CheckHolder
Hit the “Perform Test” button to calculate the required tool length

## Slide 10: CheckHolder
CheckHolder will create a dummy parallel toolpath during the calculation process
Original toolpath
Dummy toolpath

## Slide 11: CheckHolder
The “Minimum tool length” is 4.247

## Slide 12: CheckHolder
#2 Toolholder interference check
Hit the “Holder” button

## Slide 13: CheckHolder
The holder diameter is taken from the “holder dia” on the “Define Tool” dialog.
Note: HST toolpaths aren’t support at this time.

## Slide 14: CheckHolder
Hit the “Plot safe motion” to see the area’s of the toolpath that don’t have any toolholder interferences.

## Slide 15: CheckHolder
Hit the “Plot safe motion” to see the area’s of the toolpath that don’t have any toolholder interferences.

## Slide 16: CheckHolder
Hit the “Plot unreachable motion” to see the area’s of the toolpath that the tool can’t reach.

## Slide 17: CheckHolder
Hit the “Plot unreachable motion” to see the area’s of the toolpath that the tool can’t reach.

## Slide 18: CheckHolder
Go into the “Modify source operations”

## Slide 19: CheckHolder
There are four options
Select “Add manual entry”

## Slide 20: CheckHolder
The “Add manual entry” grabs the settings from the Preferences\Manual entry section
Prefix is the text output before the required tool length
Suffix is the text output before the required tool length
Note: The prefix and Suffix text will be kept as a default

## Slide 21: CheckHolder

## Slide 22: CheckHolder
Prefix
Suffix
The required tool length is outputted automatically
The manual entry operation is created and put before the selected operation.

## Slide 23: CheckHolder
Posted NC file

## Slide 24: CheckHolder
Setup Sheet
The setup sheet “overall Length” wasn’t updated since the NCI file wasn’t modified

## Slide 25: CheckHolder
Select “Change tool length” in NCI and lock operation”

## Slide 26: CheckHolder
A warning message will come up
The operation will be modified and locked

## Slide 27: CheckHolder
Setup Sheet
Modified NCI from the CheckHolder C-hook

## Slide 28: CheckHolder
Select “Create a new tool for source operation”

## Slide 29: CheckHolder
A warning message will come up
A new tool is created
Note: There is a bug in X2 where the graphics of the tool number isn’t being updated.

## Slide 30: CheckHolder
Select “Modify tool”

## Slide 31: CheckHolder
A warning message will come up
The tool will be modified for all operations that use it.

## Slide 32: CheckHolder
#3 Creating Multiple Tools and Operations
Go into preferences and select “Multiple tools” and set an increment tool length distance.

## Slide 33: CheckHolder
Creating Multiple Tools and Operations
Select the “Use minimum test tool length” and choose a starting tool length.
Note: Must hit reset if the minimum tool length is changed

## Slide 34: CheckHolder
Creating Multiple Tools and Operations
Checkholder generated 4 tools to complete the toolpath..

## Slide 35: CheckHolder
Creating Multiple Tools and Operations
Going into the “Select” will give a list of the tools that were created and their lengths
Note: Operations can be deleted from here or add additional tools.

## Slide 36: CheckHolder
Creating Multiple Tools and Operations
To add a tool length, select a tool and hit “Insert new” and a new tool length will be added.
New Tool

## Slide 37: CheckHolder
Creating Multiple Tools and Operations
Hit “Create” to generate the 3 operations

## Slide 38: CheckHolder
Creating Multiple Tools and Operations
The operation will be ghosted so it won’t be posted and 3 “Check Holder” operations are created.
1
2
3

## Slide 39: CheckHolder
Creating Multiple Tools and Operations
Operation #3 (second depth cut)
Front View
2nd Cut
2nd Cut

## Slide 40: CheckHolder
Creating Multiple Tools and Operations
Operation #4 (third depth cut)
Front View
3rd Cut
3rd Cut

## Slide 41: CheckHolder
Summary
Calculates the require tool length for an operation.
Find any interferences that the toolholder will have with the part
Break an operation into multiple operations by depth
Create additional tool or modify current tool length for deeper area’s that the original tool couldn’t reach.